VAG OBD II Connector Information

14 – LAMP LEAD

3 pin VW Mexican Beetle (Käfer) Information

(VAG 1551/1 and VAG 1551/7 Adapter Combined)

2 Notches

o        o        o                (Viewed from the end of the plug)

3	2	1

Pin		Wire Colour		Purpose

3		Red			+12 V

2		Brown			GND

1		Grey/White		K-Line (DATA)

VAG 1551/1552 Connector (5 pin DIN bayonet male)

Pin		Purpose					Connector Layout

(Solder Side)

1		K-Line (DATA)     			         3 o	     o 1

2		+12 V (do not short to K-Line !!)	             5 o      o 4

3		GND						       2 o

4		L-Line (DATA)

5		Lamp Lead (Pulse Code?)